## Slide 1: Generic Master/Slave PCB Concept
RS485-IN
RS485-OUT
5V-IN
5V-OUT
RS485 Transceiver
Opto-Isolators
MSP430
SWD
5V-IN
3-Pos
Toggle
Switch
Single Turn Pot
2x
Push
Button
2x
LED
3-Dig Display
Decoder
3.3V LDO
RST
BOOT
OSC

## Slide 2: Master/Slave Configuration
RS485-IN
RS485-OUT
5V-IN
5V-OUT
RS485 Transceiver
MSP430
SWD
3-Pos
Toggle
Switch
Single Turn Pot
2x
Push
Button
2x
LED
3.3V LDO
RST
BOOT
OSC
RS485-IN
RS485-OUT
5V-IN
5V-OUT
RS485 Transceiver
Opto-Isolators
MSP430
SWD
5V-IN
2x
LED
3-Dig Display
Decoder
3.3V LDO
RST
BOOT
OSC
MASTER
SLAVE

## Slide 3: Concept of Operation
The toggle switch chooses between No Slave, Slave A, and Slave B
  When a slave is selected, it’s LED “selected” indicator is enabled.
  When a slave is selected, the LED “status” indicator and 3-digit display readout can be modified by turning the potentiometer.
  The master indicates with LED’s whether the slave’s LED “status” indicator or the 3-digit display readout is being modified at present.
  When modifying the LED “status” indicator, rotating the potentiometer cycles the LED between being enabled and disabled.
  When modifying the 3-digit display readout, rotating the potentiometer increase or decreases the numeric value displayed.
  The master pushbuttons can either “apply” the new setting or “skip”.
The RS485 bus is optically isolated; 5V transceiver power is provided by the master. RS485 terminations are to be installed off-board, at the end of the RS485 daisy-chain.
If the master is powered into test mode, the RS485 bus may be mastered by an external driver.
The intent is to demonstrate using the MODBUS communication protocol between the master and multiple (2) slaves over RS485. It will also be demonstrated that bootloaders can be installed onto each channel such that the software may be updated over RS485.